## Slide 1: Hazard Identification, Risk Assessment, and Risk Control
Notes: Hazard Identification, Risk Assessment, and Risk Control

## Slide 2
A. Directions: Identify the type of hazards. Match Column A with Column B. Write only the letter of each correct answer on a separate sheet of paper.
Column A Column B
1. cables running across the a. mechanical hazard
floor
2. hot components or sharp b. physical hazard
edges of computers
3. inkjet printer cartridge c. electric shock hazards
4. exposed power cable d. chemical hazard
5. open casing of computer e. CRT monitor high voltage hazard
monitor
Notes: A. Directions: Identify the type of hazards. Match Column A with Column B. Write only the letter of each correct answer on a separate sheet of paper.
Column A Column B
1. cables running across the a. mechanical hazard
floor
2. hot components or sharp b. physical hazard
edges of computers
3. inkjet printer cartridge c. electric shock hazards
4. exposed power cable d. chemical hazard
5. open casing of computer e. CRT monitor high voltage hazard
monitor

## Slide 3
B. Identify the 5S principles.
1. __________________________________________________________________
2. __________________________________________________________________
3. __________________________________________________________________
4. __________________________________________________________________
5. __________________________________________________________________
Notes: B. Identify the 5S principles.

## Slide 4
PRESTEST
A. B .
1. b 1. seiri
2. a 2. seiton
3. d 3. seiso
4. c 4. seiketsu
5. E 5. Shitsuke
Notes: PRESTEST
A. B .
1. b 1. seiri
2. a 2. seiton
3. d 3. seiso
4. c 4. seiketsu
5. E 5. Shitsuke

## Slide 5: Occupational safety and health (OSH)
Is a planned system of working to prevent illness and injury where you work by recognizing and identifying hazards and risks. Health and safety procedure is the responsibility of all people in the computer and technology industries.
Notes: Occupational safety and health (OSH)
Is a planned system of working to prevent illness and injury where you work by recognizing and identifying hazards and risks. Health and safety procedure is the responsibility of all people in the computer and technology industries.

## Slide 6: There are three steps used to manage health and safety at work:
1. Spot the Hazard (Hazard Identification)
2. Assess the Risk (Risk Assessment)
3. Make the Changes (Risk Control)
Notes: There are three steps used to manage health and safety at work: 1. Spot the Hazard (Hazard Identification)
2. Assess the Risk (Risk Assessment)
3. Make the Changes (Risk Control)

## Slide 7: Using the Think Safe Steps 1. Spot the Hazard
Key Point
A hazard is anything that could hurt you or someone
else.
Examples of workplace hazards include:
 frayed electrical cords (could result in electrical shock)
 boxes stacked precariously (they could fall on someone)
 noisy machinery (could result in damage to your hearing)

## Slide 8: 2. Assess the Risk
Key Point
Assessing the risk means working out how likely it is that a hazard will harm someone and how serious the harm could be.
Notes: 2. Assess the Risk Key Point
Assessing the risk means working out how likely it is that a hazard will harm someone and how serious the harm could be.

## Slide 9: 2. Assess the Risk
Key Point
Assessing the risk means working out how likely it is that a
hazard will harm someone and how serious the harm could
be.
Whenever you spot a hazard, assess the risk by asking
yourself two questions:
Assess
 How likely is it that the hazard could harm me or
someone else?
 How badly could I or someone else be harmed?

## Slide 10: 3. Make the Changes
Key Point
It is your employer's responsibility to fix hazards. Sometimes you may be able to fix simple hazards yourself, as long as you don't put yourself or others at risk. For example, you can pick up things from the floor and put them away to eliminate a trip hazard.
Notes: 3. Make the Changes Key Point
It is your employer's responsibility to fix hazards. Sometimes you may be able to fix simple hazards yourself, as long as you don't put yourself or others at risk. For example, you can pick up things from the floor and put them away to eliminate a trip hazard.

## Slide 11: Common hazards encountered by computer technicians and users
One of the most common physical hazards involving computer technicians is cables running across the floor. If someone trips, falls, and hurts himself because of a cable you ran across the floor, someone (you, your employer, or your customer) has a serious legal negligence problem.
Notes: Common hazards encountered by computer technicians and users One of the most common physical hazards involving computer technicians is cables running across the floor. If someone trips, falls, and hurts himself because of a cable you ran across the floor, someone (you, your employer, or your customer) has a serious legal negligence problem.

## Slide 12: Common hazards encountered by computer technicians and users
If you need to temporarily run a cable across the floor, place a Danger sign similar to those "wet floor" signs used by cleaning services. For cables that are temporary but will need to run across the floor for a longer period of time,
use "gaffers tape". Gaffers tape is a heavy tape with strong adhesive to stick to the floor. It
comes in a wide range of colors, from unintrusive matte black to hazard warning red.
Although it has strong adhesive, it can be removed easily and cleanly.
Notes: One of the most common physical hazards involving computer technicians is cables running across the floor. If someone trips, falls, and hurts himself because of a cable you ran across the floor, someone (you, your employer, or your customer) has a serious legal negligence problem.

## Slide 13: Common hazards encountered by computer technicians and users
For long term cable routing there is a wide variety of cable organizing devices like cable ties, cable wraps, and cable raceways which can be used to run cable safely along the wall or ceiling.
Other common physical hazards include leaving tools on top of ladders and placing
electronic equipment in precarious positions
Notes: For long term cable routing there is a wide variety of cable organizing devices like cable ties, cable wraps, and cable raceways which can be used to run cable safely along the wall or ceiling.
Other common physical hazards include leaving tools on top of ladders and placing
electronic equipment in precarious positions

## Slide 14: Mechanical Hazards
When working on electronic equipment, ask yourself "Is there any way this equipment could hurt me?. You might stick your hand in a printer and suddenly the paper feed arm moves, feeding not only paper through the printer, but a piece of your finger too.
Notes: Mechanical Hazards When working on electronic equipment, ask yourself "Is there any way this equipment could hurt me?. You might stick your hand in a printer and suddenly the paper feed arm moves, feeding not only paper through the printer, but a piece of your finger too.

## Slide 15: Mechanical Hazards
You might move your hand past a computer chassis and lose a chunk of flesh because it is razor sharp. When working on electronic equipment always be alert to any possibility of being hurt by moving parts, hot components, or sharp edges.

## Slide 16: Chemical Hazards
Also be very careful when dealing with inkjet printer cartridges, or laser
printer toner cartridges. Ink and toner can stain skin, clothing, and carpet.
Notes: Chemical Hazards Also be very careful when dealing with inkjet printer cartridges, or laser
printer toner cartridges. Ink and toner can stain skin, clothing, and carpet.

## Slide 17: Chemical Hazards
There is a wide array of chemicals used with electronic equipment. There are display cleaning chemicals, keyboard cleaning chemicals,
compressed gas dirt and dust removers, and many
cleaning solvents. Some of these chemicals can be
harmful if accidentally swallowed, get on bare skin,
or get in eyes. Before using any chemicals for
electronic equipment always read the warnings and
instructions on the label.
Notes: Chemical Hazards There is a wide array of chemicals used with electronic equipment. There are display cleaning chemicals, keyboard cleaning chemicals,
compressed gas dirt and dust removers, and many
cleaning solvents. Some of these chemicals can be
harmful if accidentally swallowed, get on bare skin,
or get in eyes. Before using any chemicals for
electronic equipment always read the warnings and
instructions on the label.

## Slide 18: Electric Shock Hazard
Inside computers and electronic equipment, there is a range of voltages from 3.3 volts to 25 volts, most of these are harmless. But at the power supply, you'll find line voltage, which is a lethal 220 volts.
Notes: Electric Shock Hazard Inside computers and electronic equipment, there is a range of voltages from 3.3 volts to 25 volts, most of these are harmless. But at the power supply, you'll find line voltage, which is a lethal 220 volts.

## Slide 19: Electric Shock Hazard
Most of the time while working inside computers and electronic equipment, you'll want them
unplugged from the wall socket. If you need to work on equipment while it is still plugged in or powered up, remove all jewelry and wrist watches.
Notes: Electric Shock Hazard Most of the time while working inside computers and electronic equipment, you'll want them
unplugged from the wall socket. If you need to work on equipment while it is still plugged in or powered up, remove all jewelry and wrist watches.

## Slide 20: Electric Shock Hazard
If you must work inside a line power distribution box, wear an electrician’s rubber insulated gloves and safety glasses. You might think you don't need these safety devices because you are going to be extra careful, but one little slip could cause a flaming explosion that could take off your hand, embed shrapnel in your eyes, or conduct electricity through your heart,
where it takes only 10 milliamps (0.01) to kill a human.
Notes: Electric Shock Hazard If you must work inside a line power distribution box, wear an electrician’s rubber insulated gloves and safety glasses. You might think you don't need these safety devices because you are going to be extra careful, but one little slip could cause a flaming explosion that could take off your hand, embed shrapnel in your eyes, or conduct electricity through your heart,
where it takes only 10 milliamps (0.01) to kill a human.

## Slide 21: CRT Monitor High-Voltage Hazard
CRT monitors are becoming less common nowadays, but should you run into one, it is best NOT to open it up. Instead, outsource any CRT repair job to a qualified CRT repair service. A CRT monitor has a high-voltage anode inside it, which can carry a charge of up to 25,000 volts, and it can still be holding a high charge days after the power is removed.
Notes: CRT Monitor High-Voltage Hazard CRT monitors are becoming less common nowadays, but should you run into one, it is best NOT to open it up. Instead, outsource any CRT repair job to a qualified CRT repair service. A CRT monitor has a high-voltage anode inside it, which can carry a charge of up to 25,000 volts, and it can still be holding a high charge days after the power is removed.

## Slide 22
A. Direction: Read carefully each statement below. Place T on the line if the statement is
TRUE. Place F if the statement is FALSE.
_____ 1. Health and safety procedure is the responsibility of all persons in the computer
and technology industries.
______ 2. Spotting the hazards means working out how likely it is that a hazard will harm
someone and how serious the harm could be.
______ 3. If you need to temporarily run a cable across the floor, place a Danger sign similar
to those "wet floor" signs used by cleaning services.
______ 4. An LCD monitor has a high-voltage anode inside it, which can carry a charge of
up to 25,000 volts, and it can still be holding a high charge days after the power is removed.
______ 5. Inkjet printer cartridges, or laser printer toner cartridges are hazardous to users.
Notes: A. Direction: Read carefully each statement below. Place T on the line if the statement is
TRUE. Place F if the statement is FALSE.
_____ 1. Health and safety procedure is the responsibility of all persons in the computer
and technology industries.
______ 2. Spotting the hazards means working out how likely it is that a hazard will harm
someone and how serious the harm could be.
______ 3. If you need to temporarily run a cable across the floor, place a Danger sign similar
to those "wet floor" signs used by cleaning services.
______ 4. An LCD monitor has a high-voltage anode inside it, which can carry a charge of
up to 25,000 volts, and it can still be holding a high charge days after the power is removed.
______ 5. Inkjet printer cartridges, or laser printer toner cartridges are hazardous to users.

## Slide 23
B. Direction : Identify what hazard is being illustrated in the situation below .
__________ 1. Slippery computer laboratory floor
__________ 2. Hot components, or sharp edges of computer devices
__________ 3. Laser printer toner
__________ 4. Obstructed electrical cables
__________ 5. Open CRT monitor
Notes: B. Direction : Identify what hazard is being illustrated in the situation below .
__________ 1. Slippery computer laboratory floor
__________ 2. Hot components, or sharp edges of computer devices
__________ 3. Laser printer toner
__________ 4. Obstructed electrical cables
__________ 5. Open CRT monitor

## Slide 24
SELF-CHECK 1.1
A. B.
1. T 1. physical hazard
2. F 2. mechanical hazard
3. T 3. chemical hazard
4. F 4. physical hazard
5. T 5. electrical hazard
Notes: SELF-CHECK 1.1
A. B.
1. T 1. physical hazard
2. F 2. mechanical hazard
3. T 3. chemical hazard
4. F 4. physical hazard
5. T 5. electrical hazard