## Slide 1
ENVIRONMENT , HEALTH, SAFETY, & SECURITY INDUCTION COURSE
Prepared By :
_____________________
Dinesh (EHS Specialist)
Approved By :
_____________________
Tan Inn Kok ( Associate MD)

## Slide 2: Contents
1. | ASTI Introduction & Background | 14. | Fire Fighting Equipment
2. | ASTI Environmental , Health and Safety Policy | 15. | Method of Using Fire Extinguisher (P.A.S.S)
3. | ASTI Management Organization Chart | 16. | Mobile Elevating Work Platform (M.E.W.P)
4. | ASTI WSH Dept. Organization Chart | 17. | Electrical Safety
5. | ASTI Golden Rules | 18. | Working – At – Height Safety
6. | Emergency Escape Route ( For Office) | 19. | Ladder Safety
7. | Emergency Escape Procedure for Sub-Contractors ( Refer to Client SIC ) | 20. | Scaffold Safety
8. | External Emergency Services | 21. | Machinery Safety
9. | ASTI Permit-To Work System | 22. | Hot works Safety (Welding, Tag Welding Etc.)
10. | Sub-Contractors Document Submission Procedure | 23. | Occupational Diseases & Office Safety
11. | Monthly Color Coding for Equipment's | 24. | Ergonomics
12. | Personal Protective Equipment (P.P.E) | 25. | Environmental & Weather Conditions
13. | In-House Rules & Regulations | 26. | Security
14 | Environmental , Health , Safety & Security Penalty Levy | 27. | Safety Meetings

## Slide 3
ASTI Address & Contact Number
Address :
5000 Ang Mo Kio Ave 5, Singapore 569870
#04-06.
Website:
http://asti.com.sg
Contact Number:
Telephone :
+65 6482 1110
Fax :
+65 6484 2022
Scan QR Code for Directions

## Slide 4
Company's Background
Since 1997, ASTI Pte. Ltd. has been creating success stories through our multi-disciplined services that range from project management, interior design, M & E engineering to specialized engineering. Be it manufacturing plants, offices, clean rooms, data centers or laboratories, we provide turnkey solutions with end-to-end engineering capabilities. Our name is synonymous with superior quality, strong engineering competency, on-time delivery, and strong budgeting acumen that ensures cost efficiency.
In the past 20 years, we have allowed our professionalism, dedication, reliability and experience speak for us. And we are inspired to build long-term, trusting relationships rather than short-time gains.
Today, we have established our footprints on international grounds, including Malaysia, Hong Kong, China and India. Having provided specialized solutions for our clients in the pharmaceutical, manufacturing, banking and IT industries, we focus our competency on specialized solutions, particularly in establishing clean rooms, data centers and laboratories.

## Slide 5
ASTI Mission & Vision
MISSION
Asti was established with the mission to provide the industry with a highly cost effective engineering and design work in architectural, mechanical and electrical services.
VISION
Asti has made customer satisfaction our goal and superior service our priority. Our overall strategic goal is to achieve market leadership – in reputation, brand, relationships and market share, as well as environmental protection.

## Slide 6
ASTI Environmental , Health and
Safety Policy
The Management and Staff of ASTI PTE. LTD. are accountable and committed to create a safe & healthy work place for the prevention of injury and ill health to all persons working for or on behalf of ASTI PTE LTD.
We will:
Develop our management processes to ensure that Workplace Safety & Health are considered during planning and implementation.
Comply with all relevant legislation, government guidelines, regulations and industry codes of practice on Workplace Safety & Health issues, and where possible exceed them.
Ensure that on a continual basis Workplace Safety & Health hazards are identified, risks assessed and suitable controls put in place to prevent injury and ill health.
Engage with employees, contractors and visitors to further reduce safety and health hazards and risks associated with working for, with, or on behalf of ASTI PTE. LTD.
Communicate with its stakeholders its policy, objectives and targets and other relevant information pertaining to the review and implementation of the OSH-MS.
Investigate and identify causes of any incident or accident, implement and review counter measures taken to prevent reoccurrence.
Strive for continual improvement for safety and health practices and standards. This includes but not limited to regular review and monitoring of the effectiveness of this occupational health and safety policy.
To fulfill this policy, ASTI PTE. LTD. will devote resources towards setting, reviewing and achieving our WSH objectives and targets.
This policy is communicated to all employees and is available to all external bodies and members of the public.

## Slide 7
WSH Objectives/Targets
ASTI PTE LTD is committed to meet statutory and regulatory requirements through demonstration of responsibility for the safety and health of the employees, contractors, suppliers and visitors in the work environment.
To achieve this, the Management shall aim to:
Eliminate hazards at the workplace to ensure everyone’s safety and health
Prevent occurrence of incidents and ill health
Provide adequate information, training and supervision of all employees in workplace safety and health practices
Continually improve the effectiveness of the workplace safety and health management system
Comply with the requirements of the Workplace Safety and Health Act

## Slide 8
ASTI Management Organization Chart
CEO (Chief Executive Officer)
Name: Mr. Richard
Tel: 9667 9339
E-mail: km.lam@asti.com.sg
Associate Managing Director
Name: Mr. Tan In Kok
Tel: 9654 8833
E-mail: innkok@asti.com.sg
Deputy Director
Name:Mr. Wei Meng Yap
HP: 94243673
E-mail: weimeng.yap@asti.com.sg
Project Manager
Name:Mr. Kwok Chai Wong
HP: 92298453
E-mail: kwokchai.wong@asti.com.sg
Project Manager
Name: Mr. Nay Naing Zan
HP: 82994720
E-mail: nay.naing@asti.com.sg
Senior Project Manager (Electrical )
Name: Mr. Jack Hoo
HP: 97273853
E-mail: jack.hoo@asti.com.sg
Project Manager
Name: Mr. Haolin
HP: 93267163
E-mail: haolin.chen@asti.com.sg

## Slide 9
ASTI WSH Dept. Organization Chart
EHS SPECIALIST
Name: DINESH SHIVARAJ
HP: (65) 8721 2723
E-mail: dinesh@asti.com.sg
EHS COORDINATOR
Name: MATHIYALAGAN
HP: (65) 8852 8262
E-mail: mathiyalagan@asti.com.sg

## Slide 10
ASTI Golden Rules
1. FOR ALL WORKS
•
Always identifying the EHS hazards & have controls put in place before start work.
2. PERMIT-TO-WORK
•
Ensure there are valid Permit-To-work for all high risk activities
e.g Lifting Operation, Hot-Works & Confined Space before start work.
3. CRANES & LIFTING
Ensure only certified & appointed Lifting Team are doing the lifting operation.
Examine all Lifting Gears & Lifting Machine before use. Never stand under suspended load.
Always keep clear of lifting zone marked in 'Red' colour.
•
•
•
•
4. OPERATING OF MACHINERY
•
•
Do not place fingers in any pinch point of the machine. Do not use any mobile phone or devices when operating machine.
5. OPERATING OF MOBILE PLATFORM
•
•
Ensure only certified & appointed operator are operating the mobile platform .
Always be aware of other crane & pedestrians when operating mobile platform.
6. WORKING-AT-HEIGHT
Always ensure fall protection are in place before working-at-height activities start.
7. WORKING WITH ELECTRICITY
•
Always ensure no faulty or damaged electrical equipment are used & to switch off when not in use
8. WORKING WITH ENERGISED EQUIPMENT
•
Always ensure equipment are de-energized, isolated and locked out before any maintenance/repair are carry out.
9. WORKING WITH PRESSURIZED EQUIPMENT
•
Always operate pressurized equipment with design & manufactures specifications e.g. Steam-boiler, Air Compressor.
10. FITNESS FOR WORK
•
Always ensure you are not fatigued or under the influence of alcohol, drugs I prescription medication which may impair you ability to work safety before carry out any's work activities.
•
11. Reporting of any Incident/Accident or Near Miss
•
Always ensure to immediately inform any ASTI Supervisor or project personnel in-charge . Do not delay as it can lead to necessary action to be taken.

## Slide 11
Emergency Preparedness & Response
(For Office Staff)

## Slide 12
Nearest Hospital Directions
( For Office Staff)
Scan Me For
Directions

## Slide 13
Do`s & Don`ts
( For Office Staff)

## Slide 14
Emergency Escape Route
(For Office Staff)

## Slide 15
Emergency Assembly Point
(For Office Staff)
Indoor Assembly Area
AA

## Slide 16
Emergency Escape Procedure for Sub-Contractors
( Refer to Client SIC for Escape Route )

## Slide 17
Emergency Escape Procedure for Sub-Contractors
( Refer to Client SIC for Escape Route )

## Slide 18
External Emergency Services
Fire Engine
Ambulance
Police
ASTI Top Management and WSH Dept. must be informed and approve first, before any external emergency are being called.

## Slide 19
ASTI Permit-To-Work System

## Slide 20
ASTI Permit-To-Work System

## Slide 21
ASTI Permit-To-Work System

## Slide 22
ASTI Permit-To-Work System

## Slide 23
ASTI Permit-To-Work System

## Slide 24
ASTI Permit-To-Work System

## Slide 25
Sub-Contractor Document
Submission Procedure

## Slide 26
Sub-Contractor Document
Submission Procedure

## Slide 27
Sub-Contractor Document
Submission Procedure

## Slide 28
Sub-Contractor Document
Submission Procedure

## Slide 29
Sub-Contractor Document
Submission Procedure

## Slide 30
Sub-Contractor Document
Submission Procedure

## Slide 31
Sub-Contractor Document
Submission Procedure

## Slide 32
Sub-Contractor Document
Submission Procedure

## Slide 33
Monthly Color Coding for Equipment's
& Lifting Gears
S/N | Month | COLOUR
1 | JANUARY | 
2 | FEBRUARY | 
3 | MARCH | 
4 | APRIL | 
5 | MAY | 
6 | JUNE | 
7 | JULY | 
8 | AUGUST | 
9 | SEPTEMBER | 
10 | OCTOBER | 
11 | NOVEMBER | 
12 | DECEMBER | 

## Slide 34
SUBCON SUPERVISOR & ASTI STAFF
ALL SAFETY PERSONNEL
GENERAL WORKERS
Personal Protective Equipment (P.P.E)
Requirements
Cut Resistant Gloves
Safety Goggles
Safety Vest
Earplugs

## Slide 35
ASTI Personal Protective Equipment
(For All Project Sites)
Compulsory to wear Safety Helmet with Chin Strap, Safety Shoes, Reflective Vest , Hand Gloves and Safety Goggles.
Safety Helmet
ASTI Safety Vest
Safety Boots
Cut Resistant Gloves
Safety Goggles

## Slide 36
In-House Rules & Regulations
Wear and Use PPE
Follow Safe Work Procedure
Report Unsafe Act and Unsafe Condition,
Report Near Miss, Accident and Incident
Don’t tamper any safety devices
Implement Risk Control Measures

## Slide 37
In-House Rules & Regulations

## Slide 38: In-House Rules & Regulations
Alcoholic beverages on Company’s Project Sites are not allowed.
Anyone found to drunkard, will be fined and banned from entering ASTI Project Sites.

## Slide 39: In-House Rules & Regulations:
WSHE MANDATORY SIGNS
Fire Extinguisher
WARNING SIGNS
INFORMATION SIGNS

## Slide 40: In-House Rules & Regulations: Work Behavior
Take Safety Seriously
No horseplay is allowed at all times within the workplace
No Fighting will be allowed in the workplace. Offenders will be handed over to Singapore Police Force for investigation and will be banned from ASTI Project Sites

## Slide 41: In-House Rules & Regulations: Contraband Items
Offenders will be handed over to Singapore Police Force for investigation and will be banned from ASTI Project Sites

## Slide 42
In-House Rules & Regulations:
Compulsory SIC for All new Staff & Sub-Contractors
ASTI Safety Inducted Sticker
Discipline of Work Stickers for Helmet (Pasted Front and Back)

## Slide 43
Environmental , Health , Safety &
Security Penalty Levy

## Slide 44
Environmental , Health , Safety &
Security Penalty Levy

## Slide 45
Environmental , Health , Safety &
Security Penalty Levy

## Slide 46
Environmental , Health , Safety &
Security Penalty Levy

## Slide 47
Environmental , Health , Safety &
Security Penalty Levy

## Slide 48
Environmental , Health , Safety &
Security Penalty Levy

## Slide 49
Fire Fighting Equipment
No personnel is to temper, trigger or use the fire fighting device or equipment unless in emergency situation with the authorization of ASTI Management for conducting emergency fire drill purposes.
Any personnel found to misusing , tempering or triggering the fire fighting device or equipment in an non-emergency situation or without the authorization of ASTI Management will be held liable and dealt accordingly by the management

## Slide 50
Method of Using Fire Extinguisher (P.A.S.S)

## Slide 51
Mobile Elevating Work Platform
Safety
(M.E.W.P)

## Slide 52
Mobile Elevating Work Platform (M.E.W.P)

## Slide 53
Mobile Elevating Work Platform (M.E.W.P)

## Slide 54
Mobile Elevating Work Platform (M.E.W.P)

## Slide 55
Mobile Elevating Work Platform (M.E.W.P)

## Slide 56
Mobile Elevating Work Platform (M.E.W.P)

## Slide 57
Mobile Elevating Work Platform (M.E.W.P)

## Slide 58
Case Study:
Unsafe Use of Fork Lift

## Slide 59
Work-At-Height
Safety
(WAH)

## Slide 60
Work-At-Height Safety
Fall Prevention Plan
Work at Height Permit
Competent Work at Height Personnel
Standing Supervision
Pre-Use Inspection

## Slide 61
Work-At-Height Safety



Workers using M.E.W.P without wearing proper PPE and wrong anchorage point for safety harness.
Tools kept on platform ladder obstructing the usage of it. Tools can fall down and hit somebody.
Messy environment, ground unstable and worker never use P.P.E.

## Slide 62
Work-At-Height Safety


Working area properly barricaded
Buddy System In-Place
Standing Supervision
Proper P.P.E worn
Proper Anchorage point for Safety Harness used


## Slide 63
Work At Height Safety

## Slide 64
Work At Height Safety

## Slide 65
Case Study:
Incompetent Usage of M.E.W.P

## Slide 66
Ladder Safety
(WAH)

## Slide 67
Ladder Safety

## Slide 68
Ladder Safety

## Slide 69
Ladder Safety
NOTE: A frame ladder or fireman ladder is only used for access or for light works using one hand and always maintaining 3-point contact on Ladder.
If need to work using both hands it is mandatory to for contractors to provide Platform ladder at the sites.

## Slide 70
Case Study:
Unsafe Use of Ladder

## Slide 71
Electrical Safety

## Slide 72: ELECTRICAL SAFETY

## Slide 73: ELECTRICAL SAFETY
Only trained electricians are allowed to perform repair works on electrical systems.
LOTO

## Slide 81
Electrical Safety
All electric powered tools and equipment including using direct current (D.C) and load exceeding 45 kVA for non-domestic purposes MUST be inspected and approved by a Licensed Electrical Worker (L.E.W) before use.
All electric powered tools and equipment including using direct current (D.C) and load exceeding 45 kVA for non-domestic purposes MUST be re-inspected at least once a month or after repair by a Licensed Electrical Worker (L.E.W).
All electric powered tools and equipment MUST have valid L.E.W inspection sticker before use.
Electric powered tools and equipment with damaged or missing parts MUST not be use until it is recertified by an have Licensed Electrical Worker (L.E.W).

## Slide 82
Control of Explosive Power Tools Use
Special Authorization required to Use Explosive power tools at ASTI Project Sites.
ASTI WSH Department need to approve SWP and RA if ASTI Management authorise contractors to use

## Slide 83
Electric wire must be elevated at least 02 meters above ground or floor level with insulated hooks or wire-stand when reasonable and practicable.
Poor wire management, may lead to tripping hazard.
ü
ü
Good Cable Management System
X

## Slide 84
Case Study:
Electrocution due to Wet Cable

## Slide 85
Scaffold Safety

## Slide 86: Scaffold Tag
Scaffold Tag is only valid for 7 days. Before the expiry date, Scaffold Supervisor must renew the tag.
Safety Harness to be worn at all times.
100% Tie off on the scaffold to be done at all times.
X
ü

## Slide 87: Scaffold Safety
Safety Harness must be valid for 3 years.
All harness to be inspected before use by main con safety. Individual supervisors to do their prior checks.
ü
X
X

## Slide 88: Safe use of Scaffold
X
ü
ü
Use proper access to climb up or down scaffold
Wear your safety harness and secure it to an anchorage point.
DO NOT use shortcuts, they are unsafe.

## Slide 89: Safe use of Scaffold
DO NOT use a damaged harness.
DO NOT move a mobile scaffold when somebody is on it. Ensure to apply the brakes.
Practice good housekeeping. Tripping or slipping may lead to falling from height.
X
X
X

## Slide 90: Safe use of Scaffold
DO NOT sit or lean on guardrails.
DO NOT use scaffolds without top and/or mid guardrails. Check that scaffolds are tagged and certified safe by Scaffold Supervisor before use.
Obey all warning signs.
X
X
ü

## Slide 91: Safe use of Scaffold

## Slide 92
Machinery Safety

## Slide 93: Machine Guarding
Moving parts on machinery must be guarded.
Don’t remove the guards.
Inform foremen / safety personnel immediately.
X
ü

## Slide 94
Other Machinery Safety
Competent and Authorised Operator
Permit To Work
Cordon off Danger Zone
Pre- Operation Check
Regular On The Job Training

## Slide 95
Machinery Hazards

## Slide 96
Preventing Machinery Hazards

## Slide 97
Preventing Machinery Hazards

## Slide 98
Machine Safety

## Slide 99
Case Study:
Forklift Overturned

## Slide 100
Fire and
Hot Works Safety

## Slide 101: Hot Works Safety
Hot work permit
Daily checklist
Cylinder cage/trolley with chain
Fire extinguisher
Fire Blanket
Warning signs
Personal Protective Equipment
  ( Face Shield, Goggles, hand gloves)
Earthing for welding machine
No damage gauges
X
Damaged gauge

## Slide 102: Hot Works Safety
Ensure all welding works have proper fire extinguisher, fire blanket & Face shield
X
ü

## Slide 103
Case Study:
Acetylene gas explosion

## Slide 104
Occupational Diseases &
Office Safety

## Slide 105: Occupational Diseases

## Slide 106: Occupational Diseases

## Slide 107: Occupational Diseases

## Slide 108
Occupational Diseases –
Appropriate Hand Gloves
Source: LTA Safety News letter

## Slide 109: Occupational Diseases – How to wear a Ear plug

## Slide 110: Office Safety

## Slide 111: Office Ergonomics

## Slide 112
Ergonomics

## Slide 113: Ergonomics

## Slide 114: Ergonomics – Manual handling

## Slide 115: Ergonomics – Manual handling

## Slide 116: Ergonomics – Manual handling

## Slide 117
Environmental &
Weather Conditions

## Slide 118: Environmental & Weather Conditions

## Slide 119: Environmental & Weather Conditions

## Slide 120: Environmental & Weather Conditions

## Slide 121: Environmental & Weather Conditions

## Slide 122
Security

## Slide 123: SECURITY RULES & REGULATIONS
All Contractors are to prepare their NRIC/WP Card in order to change to change pass at the respective ASTI project sites (Where deem necessary)
No exchanging of passes shall be done.
Passes must be always displayed.
Incase, if pass were to be misplaced or lost, Immediately inform supervisor in charge and report to the guard house.

## Slide 124: SECURITY RULES & REGULATIONS
NO
Drugs on ASTI`s Project Sites are allowed.
Offenders can be dismissed and/or arrested.

## Slide 125
Safety Meetings (On-Site)
Daily Toolbox Meeting
Weekly Mass Tool Box Meeting
Weekly EHS Inspection report
Monthly EHS Committee Site Walk

## Slide 126
Employees Rights
YOU ALWAYS HAVE THE RIGHT TO REFUSE UNSAFE WORK

## Slide 127
Wait, I have some questions for you !

## Slide 129: Thank you for your time and work safely !